## Slide 1: Knowledge Engineering for Robot Capabilities

## Slide 2: Motivations
Robotics systems are coming to commercial use
Complexity of robotics systems for non-experts
Usage of robots as a platform, not as end product

## Slide 3: Motivations
GOAL: a semi-automatic layer of knowledge engineering to make sense of the robotics systems
High-level robot capability representation is fundamental for multi-purpose multi-robot planning (or coordination)
This may lead to a required standardization (both in ROS and in designing robot capabilities)

## Slide 4: ROS: Robot Operating System
Middleware for robotics
Component-based
Publish-subscribe paradigm
Thriving community
Exploration tools

## Slide 5: ROS Main elements
Asynchronous communication based on messages exchanged on named channels
ROS component
Atomic element encapsulated in a single executable
Data type of the data exchanged on the channels
NODE
TOPIC
NODE
NODE
MESSAGE
publish
subscribe
SERVICE
Synchronous request from a component to another

## Slide 6: ROS Architecture
joy_node
/joy
Joy.msg
/cmd_vel
Twist.msg
joy_to_cmd
robot_driver
Joypad driver provided by ROS
Standard message
(teleoperation)
User developed component
Interface to the robot
Standard message
(robot control)
Architecture of a simple robot piloted directly by the user using a joypad

## Slide 7: Robot Capability Ontology
Node
Communication component
ServiceClient
ServiceServer
Publisher
Subscriber
Message
Topic
Service
SrvMsgRequest
SrvMsgResponse
SrvMessage
publishes/subscribesTo
communicatesThrough
offers/requests
isA
isA
isA
isA
publishedIn/readFrom
consumers
produces
defines
partOf
partOf
creates
receives

## Slide 8: Robot Capability Ontology
Capability
Sensing
Movement
Representation
…
Body Movement
Navigation

## Slide 9: Robot Capability Ontology
Capability
Message
/ImageRaw
Sensing
Vision

## Slide 10: Possible Evaluation
Use an engineering approach (no claim on the ontology)
  e.g. how much the development time is reduced
  e.g. how much does the automation work
An interface to the robot capabilities
Different robots do different things without a previous expertise
  e.g. users have to give 3 tasks to 3 different robots through the same interface